| Overview: |
| --- |
| This project assumes the teacher and students have already completed the Digital Mood Ring*. In this project, students build and program a simple feedback and control loop. This engineering principle is central to many industrial systems and consumer products. The system uses three input modules; Two temperature sensors and a Hall effect sensor which responds to a magnetic field. The system has four outputs that include two white LED lights (headlights), 1 continuous servo (controls the window) and also makes use of the TI-Innovator Hub’s built-in speaker (horn honking). The continuous servo requires more power than the calculator can provide so an external USB battery is required. A program is written to read all three input parameters and logically compare them with critical set-point values to determine when to turn on the alarm system. The project is presented in a series of small challenges that build the knowledge and skills required for the final open-ended challenge. The final challenge also relies on the students’ understanding of important biology and Earth science topics that are relevant to optimizing the system the students ultimately design and refine. * The Digital Mood Ring is a series of challenges that build the conceptual knowledge and skills needed to complete subsequent projects. The materials for the Digital Mood Ring project can be found here - http://bit.ly/2oqU1X8 |
| Possible NGSS topics to explore with students: |
| Disciplinary Core Ideas: HS-LS1-3 – Mechanisms of homeostasis MS-ETS1-1 to 1.4 – Engineering design MS-PS3-3 – Design that maximizes thermal energy transfer | Science & Engineering Practices: Asking questions & defining problems Evaluate competing designs Constructing explanations & designing solutions | Crosscutting Concepts: Systems & System Models Cause & Effect Energy & Matter |
| Background: |
| Light to Heat Each summer, there are horrifying stories of children and pets left in hot cars. Ultimately, most end up having a heat stroke and in many cases pass away. The inside of a car heats up so much faster than the outside due to a similar mechanism as the greenhouse effect. As rays of sunlight stream into the vehicle through the windows, the light strikes the surfaces of the interior of the car. That light energy is transformed into infrared energy which is trapped inside the car and causes the temperature inside to increase much more quickly than outside. Unlike light rays, infrared radiation has a bigger wavelength. The wavelength is big enough that they are unable to escape back through the windows and are therefore trapped inside the car. Stayin’ Cool! Mammals such as humans, dogs, and cats have the ability to thermoregulate to maintain homeostasis. However, if those thermal regulation mechanisms are unable to keep up with an environment that continues to warm, such as the inside of a car, that mammal will eventually go into heat distress. Humans can sweat to help increase the removal of heat from the body through evaporation. Dogs usually pant to remove heat although they also have a small amount of sweat glands in the pads of their paws also. Cats will sprawl out on surfaces that are relatively cool to help remove body heat. They will also lick their paws and rub the saliva on warmer parts of their bodies to increase evaporative cooling which is a similar mechanism as sweating in humans. Humans, dogs, and cats all have ways to regulate temperature but usually not at a rate that can offset how quickly the inside of a closed car during the warmer months will increase in heat. The problem with too much heat Brain impairment, dehydration, heart failure, cell swelling, and protein denaturation can all occur causing big problems…and potentially death. Every summer these stories occur. Research more about why mammals such as humans, dogs, and cats are unable to endure hot environments like closed cars in the summer for long periods of time. Then design a solution using technology to deal with this problem. Refine your design until you have a working prototype. With your teacher’s permission, compare your prototype with those of your classmates to determine which team has the “best” system. |

| Command Example Behavior DispAt <line #> , <”text”> , <variable name> DispAt 3, “Temperature = ”, t When variable t has a value of 26, the following line is displayed on the calculator: Temperature = 26 (temp readings are in °C by default) Wait <number> Wait 3 Wait will pause the program for a specified number of seconds. Wait 3 means the program will pause for 3 seconds. CONNECT <type> <number> TO <port> Send “CONNECT TEMPERATURE 1 TO IN1” Associates the first TEMPERATURE object with a temperature module plugged into port IN1 on the Hub. SET <type><number> TO <value>. Send “SET LED 1 TO ON” Turns on LED 1. Other parameters may include BLINK <rate> TIIME<duration> “SET LED 1 ON BLINK 3 TIME 20” READ <type> <number> Send “READ TEMPERATURE 1” Reads a measurement from the first temperature object. Get <variable> Get t Stores the temperature measurement into a variable named t. The value stored will contain the measurement from the immediately preceding READ command. Note: a Get command must immediately follow a READ command. For <counter variable>,<start value>,<end value>,[<step value>] <statements> EndFor For n,1,10 DispAt 3,n EndFor Runs For loop 10 times, starting at 1 and ending at 10. Executes the statement in the block each time, displays the value for the counter variable on row 3. While <Boolean expression> <statements> EndWhile key:=“ ” While key≠“esc” READ “TEMPERATURE 1” Get t DispAt 3,“Temperature= “,t key:=getKey() Wait 1 EndWhile The statements in the While loop are executed until the escape key is pressed. The While loop continues as long as the Boolean expression evaluates to “true”. The variable key is set to an initial value of an empty string using the assign function, “:=”. getKey() is a function that returns a string with the name of the last key pressed while a programming is running. In this program the value of getKey() is stored to the variable key. If <Boolean expression> Then <statements> EndIf If t>26 Then Send “SET COLOR 255 128 0” EndIf Checks to determine if the value of variable t is greater than 26. If the statement is true then the block of commands in the If..EndIf block are executed. Otherwise the block is skipped. In this case, when the temperature is greater than 26 the calculator will send a command to the TI-Innovator to set the COLOR to be yellow. <Boolean expression> and <Boolean expression> If t≥22 and t<24 Then Send "SET COLOR 0 255 0" EndIf When both expressions are true the “and” function is “true” and the statements are executed. Otherwise, the function returns false and the statements are skipped. |
| --- |
| See TI-Innovator Technology eGuide for more background https://education.ti.com/html/webhelp/EG_Innovator/EN/index.html |
| Setup Project: | Supplies: |
|  | Calculator Unit to Unit Cable TI-Innovator Hub Grove Cable x5 Grove Temperature sensor x2 Fashion Doll Car, shoebox, or other object to model a car Grove Hall Sensor Grove White LED Light x2 Grove Continuous Servo External USB Battery w/ Cable |  |

| Student Activity: | Teacher Notes: |
| --- | --- |
| Challenge 1: Write a program that will play two sounds for 1 second each in a For loop that repeats five times. e.g. Send “SET SOUND 220” | Teacher Guidance during Challenge 1: Use a For..EndFor loop to alternate between two different sound frequencies one octave apart. Loops are used to repeat a set of command. A For loop repeats a specified number of times. In TI-Basic the programmer defines a For loop with four inputs: a counter variable, a beginning value for the counter variable, an ending value for the counter variable and an optional step value variable. For…EndFor is found on the Program Control Menu Use the Wait command to determine how long each tone plays Example program: Define pc1()= Prgm For n,1,10 Send "SET SOUND 440" Wait 1 Send "SET SOUND 880" Wait 1 EndFor EndPrgm Try adding a third tone in your program Try to find the limits of the built-in speaker by changing the frequencies |
| Challenge 2a: Use a For..EndFor to blink two external LED’s. | Teacher Guidance during Challenge 2: The Hub Connect commands provide the hub with information about the type of device plugged into external ports and how to communicate with that device. Connect LED’s to OUT 1 and OUT 2 on the Hub Use the Send “CONNECT LED # TO OUT #” command Use a For..EndFor command to make the LED’s turn off and on Example program: Define pc2a()= Prgm Send "CONNECT LED 1 TO OUT 1 " Send "CONNECT LED 2 TO OUT 2 " For n,1,30 Send "SET LED 1 ON" Send "SET LED 2 ON" Wait 1 Send "SET LED 1 OFF" Send "SET LED 2 OFF" Wait 1 EndFor |
| Challenge 2b: Try Challenge 2a once more using the “BLINK” and “TIME” options. This time you can do it without a For..Loop. | Example program: Define pc2b()= Prgm Send "CONNECT LED 1 TO OUT 1 " Send "CONNECT LED 2 TO OUT 2 " Send "SET LED 1 ON BLINK 3 TIME 30" Send "SET LED 2 ON BLINK 3 TIME 30" Wait 30 EndFor |

| Challenge 3: Connect a continuous servo motor to the TI-Innovator Hub and cause it to rotate clockwise (CW) and then in the opposite direction, counterclockwise (CCW). | Teacher Guidance during Challenge 3: Use a For..EndFor loop to cause a continuous servo motor to rotate clockwise and then counterclockwise. Use Send “CONNECT SERVO.CONTINUOUS # TO OUT 3” Use CCW or CW to set the direction of the continuous servo (note – you can also use positive/negative to set direction…positive doesn’t require a “+”). Power for the continuous servo motor is already ranged from 0 to 100; 0 being off and 100 being full on. After CCW or CW, use a number between 0 (off) to 100 (full power) Be sure external battery is attached to PWR and turned on just before running program. Example program Define c3()= Prgm ©Be sure to add an external battery to the PWR port on the TI-Innovator Hub Send "CONNECT SERVO.CONTINUOUS 1 TO OUT 3" For n,1,5 Send "SET SERVO.CONTINUOUS 1 CW 20 TIME 1" Wait 1 Send "SET SERVO.CONTINUOUS 1 CCW 20 TIME 1" Wait 1 EndFor EndPrgm Experiment with changing the power and TIME duration to see what effect that has on how many turns the servo will make. |
| --- | --- |
| Challenge 4: Connect a temperature sensor to the TI-Innovator Hub and display the temperature on the calculator. | Teacher Guidance during challenge 4: The Read command instructs the Hub to read a value from the device plugged into the specified port. The Hub places that value in memory on the Hub, waiting for the calculator to “get” the value. The Get command retrieves the value from the Hub and stores it to the variable named in the command. The While..EndWhile loop is similar to a For loop except instead of repeating a certain number of times, it continues to loop until a predefined condition exits the loop. Note that multiple arguments can be used to build a message with the DispAt command. Example program: Define c4()= Prgm Send "CONNECT TEMPERATURE 1 TO IN 1" key:=“ ” DispAt 8,“Press [esc] to Quit” While key≠“esc” Send "READ TEMPERATURE 1" Get temp DispAt 3,"Temperature=",temp,“°C” Wait 0.5 key:=getKey() EndWhile EndPrgm |
| Challenge 5: Connect the Hall sensor, which determines if the south pole of a magnetic field is close to the sensor. Display “Magnet is not present” or “Magnet is present” based on the READ of the Hall sensor and the position of the magnet. | Teacher Guidance during Challenge 5: Some sensors or output devices do not have an associated object that can be found in the input and output menus. For these devices we use ANALOG.IN, DIGITAL.IN, ANALOG.OUT, or DIGITAL.OUT. The Hall sensor detects the presence (or absence) of a magnetic field with south polarity. For the Hall sensor you will use ANALOG.IN. Values reported are related to voltage measurements. Values lower than 100 typically represent the presence of south polarity of a magnetic field. Values above 6,500 typically represent the absence of south polarity of a magnetic field. It is recommended that IN3 is used to supply enough power to the sensor. Example program: Define c5()= Prgm Send "CONNECT ANALOG.IN 1 TO IN 3” ©ANALOG.IN 1 is the object for the Hall Effect magnetic proximity sensor While key≠“esc” Send “READ ANALOG.IN 1” Get m If m>100 Then DispAt 5,“Magnet is not present” Else DispAt 5,“Magnet is present” EndIf Wait 0.5 key:=getKey() EndWhile EndPrgm |
| Challenge 6: Use the skills developed from challenges 1 through 5 to develop an alarm system for a model of a car that determines if both a pet is present (magnet) AND the temperature reading inside the car reaches a critical threshold before triggering the alarm. | Teacher Guidance during Challenge 6: This challenge has students create a system that reads data from inputs such as temperature and the hall sensor which in turn controls LED’s, sounds through the speaker, and the continuous servo motor. Notice that While..EndWhile is used often with sensors (inputs) and If..EndIf is used with outputs. Example program: Define c6()= Prgm key:=“ ” window:=1 Send “CONNECT TEMPERATURE 1 TO IN1” Send “CONNECT TEMPERATURE 2 TO IN2” Send “CONNECT ANALOG.IN 1 TO IN3” Send “CONNECT LED 1 TO OUT1” Send “CONNECT LED 2 TO OUT2” Send “CONNECT SERVO.CONTINUOUS 1 TO OUT3” DispAt 1,“Pet Car Alarm is now monitoring safety” DispAt 8,“Hit ESC to quit monitoring car” While key≠ “esc” Send “READ TEMPERATURE 1” Get temp_in Send “READ TEMPERATURE 2” Get temp_out Send “READ ANALOG.IN 1” Get hall DispAt 4,“Pet Sensor= ”,hall,“bits” DispAt 5,“Temperature inside car= ”,temp_in,“°C” DispAt 6,“Temperature outside car= ”,temp_out,“°C” If temp_in>25 and hall<100 Then Send “SET LED 1 ON BLINK 3” Send “SET LED 2 ON BLINK 3” Send “SET SOUND 400 TIME 2” Send “SET SOUND 800 TIME 2” If window=1 Then Send “SET SERVO.CONTINUOUS 1 30 .25” window:=0 EndIf DispAt 2 “Warning! Pet is in heat distress!” Else Send “SET LED 1 OFF” Send “SET LED 2 OFF” Send “SET SOUND OFF” If window=0 Then Send “SET SERVO.CONTINUOUS 1 -30 .48” window:=1 EndIf If hall<500 Then DispAt 2,“Pet inside car and happy” Else DispAt 2,“Pet not inside car” EndIf EndIf key:=getKey EndWhile Send “SET LED 1 OFF” Send “SET LED 2 OFF” Send “SET SOUND OFF” Send “SET SERVO.CONTINUOUS 1 0” DispAt 1,“Pet Car Alarm is OFF” EndPrgm |